## Slide 1: Approximate quantities
For Elemental Cost Planning

## Slide 2: Elements
Quantity surveying elemental measurement need to fulfill the following requirements:
Quickness in preparation
Accuracy
Capability of adjustment for design change
ANZSMM2018 is used for producing schedules of quantities not for estimates. A reasonable method of measurement is required for estimates. They should be kept in the simplest of form possible so they are accurate and quick to prepare. Remember the drawings available are no more than sketches so detailed quantities are out of the question

## Slide 3: Estimates
Note:
Difference between quantity surveying estimates and builders estimates are that consultant QS are trying to predict the main contractors tender whereas the main contractor is trying to forecast what the actual project is going to cost them to build.

## Slide 4: Three levels of estimating
Three distinct levels of estimating
Elemental rate - Unit cost of element based on GFA
Element unit rate based on area
Sub element unit rate based on specific quantity for each sub element (different specs)

## Slide 5: Three levels of estimating

## Slide 6: Measurement - Approximate quantities.
Measuring for cost planning requires you to be quick and accurate
Bulk quantities provide the means to achieve this
In using bulk quantities the measuring detail is transferred to the rating detail

## Slide 7: Units of Bulk Quantities
Elemental Analysis of Costs of Building - set up a list of bulk quantity units.
Example - concrete columns – The unit is m.
- Pad footing – No.

## Slide 8: Hierarchy of information

## Slide 9: All inclusive rates
All-inclusive rates can be established for the items by analysing priced schedules, Price books, journals.
The rate for concrete columns would include concrete, formwork, reinforcing steel, and all sundry connected work.
Concrete floor slabs on grade - includes concrete, edge formwork, reinforcing mesh, hard fill, damp proof membrane and sand blinding.

## Slide 11: Rates

## Slide 12: Spreadsheet template

## Slide 13: Spreadsheet
Description
Units of quantity
Side notes
LxBxHxMultiplyer (layout)
Terms
Dimset(s)
UoM

## Slide 14: Spreadsheet
Zone 1 Description & side-notes

## Slide 15: Spreadsheet
Zone 2 Calc & quantity columns

## Slide 16: Spreadsheet
Zone 3 Pricing Description & side-notes