## Slide 1: Elemental Analysis of Costs of Building Projects

## Slide 2
New Zealand Institute of Quantity Surveyors (Inc.)
Call NZIQS:
0800 4 NZIQS (0800 469 477) or 04 473 5521
Write to NZIQS:
office@nziqs.co.nz
The Executive Director P O Box 10469
The Terrace Wellington 6143
Find NZIQS at:
Level 8, 108 The Terrace BERL House
Wellington 6011
Map: www.nziqs.co.nz/About/Contact
More Information about NZIQS:
www.nziqs.co.nz
Elemental Analysis Editions:
© New Zealand Institute of Quantity Surveyors (Inc.), 2017
Except as provided by the Copyright Act 1994, no part of this publication may be reproduced or stored in a retrieval system in any form or by any means without the prior written permission of the copyright owner.
Whilst every care has been taken in compiling this handbook, NZIQS accepts no responsibility for any errors or omissions herein.
Revision Ref | Date | Revision Outline
1st edition | 1970 | 
2nd edition | 1974 | 
3rd edition | 1982 | 
4th edition | 1992 | 
Reprinted | 2012 | 
5th edition | January 2017 | Element E28 Other Development Costs
added,

## Slide 3: Contents
Page 3
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
17
Introduction
Introductory Notes
Definitions and General Notes
Summary of Elements
Structure Exterior Fabric Interior Finishing Services
External Works and Sundries P&G, Margins and Contingencies
Form and Extent of Elements
E1 Site Preparation E2 Substructure
E3 Frame
E4 Structural Walls E5 Upper Floors E6 Roof
E7 Exterior Walls and Exterior Finish E8 Windows and Exterior Doors
E9 Stairs and Balustrades E10 Interior Walls
E11 Interior Doors E12 Floor Finishes E13 Wall Finishes E14 Ceiling Finishes
E15 Fittings and Fixtures E16 Sanitary Plumbing
E17 Heating and Ventilation Services E18 Fire Services
E19 Electrical Services
E20 Vertical and Horizontal Transportation E21 Special Services
E22 Drainage
E23 External Works E24 Sundries
E25 Preliminaries E26 Margins
E27 Contract Contingencies
E28 Other Development Costs
Standard Forms Project Summary Project Analysis
Element Unit Rate Record Sheet
List of Groups, Elements, Sub-elements
18
19
20
21
22
23
24
25
26
28
29
31
32
33
34
35
36
37
38
39
40
41
42
43
44
4
4
4
5
5
5
5
6
6
7
8
8
9
11
13
14
15
16
17

## Slide 4
Page 4
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Introduction: Introductory Notes
Introduction
Introductory Notes
The accompanying text provides a standard for the preparation of cost analyses and for the uniform recording of cost information intended for use in elemental cost planning.
Definitions and General Notes
Element
An element is a component part of a building or a development which, irrespective of design or method of construction, tends to perform the same function.
Gross Floor Area
The area used for the calculation of element costs is the gross floor area, measured over all the exterior walls of the building, over partitions, columns, interior structural or party walls, stair wells, lift wells, ducts, enclosed roof top structures and basement service areas. All exposed areas such as balconies, terraces, open floor areas and the like are excluded.
Generally, projections beyond the outer face of the exterior walls of a building such as projecting columns, floor slabs, beams, sunshades and the like shall be excluded from the calculation of gross floor areas.
Where the outer face of the exterior walls of a building are not regular vertical surfaces, the overall measurements shall be taken at floor levels and note made of the vertical profile of the wall line.
Where mezzanine floors occur within a structure the gross floor area of this mezzanine shall be added to all other complete floor areas and become a constituent part of the gross floor area.
Net Rentable/Tenantable Area
This is the area available for occupation less public circulation spaces, plant and service areas and the like.
Wall to Floor Ratio
In the calculation of enclosing wall to floor ratio, the height of the wall should be calculated from the lowest floor slab level to the highest ceiling level. The floor area should be the gross floor area. The wall to floor area should be expressed as a ratio, to two decimal places:
enclosing wall area (W) gross floor area (F)
Quantity of Element Unit/Element Unit Rate
It is found convenient to express some elements in a unit of area related just to that element, e.g. ‘Substructure’ as a cost per m2 of the lowest floor area, or ‘Roof’ as a cost per m2 of a roof area. Refer to Form and Extent of Elements for the definition of these areas.
Quantity of Sub-element Unit/Sub-element Unit Rate
Each sub-element within an element should be quantified to the unit measure indicated. Refer to Form and Extent of Elements for the definition of unit of measurement.
Divisors
Elemental Rate =
Element Unit Rate =
Sub-element Unit Rate =
Total Cost of Element Gross Floor Area
Total Cost of Element Quantity of Element
Total Cost of sub-element Quantity of sub-element

## Slide 5
Page 5
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Summary of Elements: Structure
Summary of Elements
Structure
Site Preparation
All work necessary to clear a site of existing structures, trees, etc. to create a suitably benched surface as a working platform and to support adjoining structures.
Substructure
All work below the underside of the lowest floor finish, including all work applicable to the foundations, hardfilling beneath floor slabs, concrete floor slabs, service ducts, lift pits and the like. Includes basement walls between different levels. Excludes excavation above lowest floor level, plumbing, drainage and other services below lowest floor finish.
Frame
All load bearing column and beam framework above lowest floor finish, major roof framing members such as rafters, joists. Excludes all profiled finishes and all applied finishes.
Structural Walls
Load bearing and diaphragm walls together with integral columns. Excludes non-structural spandrel panels, linings and applied finishes and treatments, profiled finish.
Upper Floors
Suspended floors, mezzanine floors, balcony floors and roof slabs. Includes fairface finish to concrete floor and roof slabs. Excludes floor support beams and soffit treatments.
Exterior Fabric
Roof
Complete weatherproof covering of all types to roofs. Includes decks; diaphragm bracing, sarking and screeds; roof support components such as roof purlins, battens; insulation to underside of roof covering, verge and eaves facing and soffit; secret, parapet and eaves gutters, downpipes, roof lights. Excludes support beams; in situ or precast concrete roof slabs; parapets and parapet finishes, gable and gable finishes; canopies, balconies, covered ways, roof top structures.
Exterior Walls and Exterior Finish
All work to exterior walls, including applied or in situ finishes. Includes gable ends, parapets, spandrels and finishes; both skins of exterior cavity walls; applied exterior finishes to exterior columns, beams, structural spandrels and walls. Excludes curtain walls.
Windows and Exterior Doors.
All windows and doors in exterior walls, including vertical or near vertical glazing. Excludes roof lights, interior glazed screens, curtain pelmets, sun screens, curtains, tracks and blinds.
Interior Finishing
Stairs and Balustrades.
Flights and intermediate landings including integral finishings, handrails and balustrades. Excludes applied finishes.
Interior Walls.
All non-structural internal walls including glazed screens, demountable partitions and sound and fire walls. Excludes fanlights and sidelights, folding or sliding doors forming partitions, wall finishes, and fire stopping and sound barriers in ceiling spaces, where these are a continuation of partitions below the ceiling line.

## Slide 6
Page 6
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Summary of Elements: Services
Interior Doors.
All interior doors including frames, architraves, finishes, glazing, fanlights, side lights, panels over doors, hardware and control systems. Excludes doors to proprietary partition systems, fittings and fixtures.
Floor Finishes.
Includes all preparatory work, screeds, surface finishes, matwells, threshold strips, raised floors laid over structural floors.
Wall Finishes.
Includes all preparatory work and finishes to interior walls, isolated columns, and to interior faces of exterior walls. Excludes fairface finish to concrete, finishes to proprietary partition systems. Includes skirtings, cornices, trims, dado rails and the like.
Ceiling Finishes.
Includes all preparatory work and finishes, suspended ceilings and framing, soffits of staircases and intermediate landings. Excludes ceiling framing forming part of roof framing.
Fittings and Fixtures.
Joinery fittings, whether built-in or fixed in position, includes glass, hardware and finishes. Excludes sanitary fittings, electrical fittings, services to fittings and fixtures.
Services
Sanitary Plumbing.
Hot and cold water supply, including hot water cylinder, sanitary fittings, soil, waste and vent pipes. Excludes special kitchen equipment, laboratory equipment and services.
Heating and Ventilation Services.
Heating, ventilation and air conditioning systems, including all associated equipment. Excludes heating source to hot water system.
Fire Services.
All fire services within a building, including all associated electrical work.
Electrical Services.
All electrical services providing lighting and power. Excludes lighting and power to external works; wiring to equipment and machinery which is covered in other elements.
Vertical and Horizontal Transportation.
Vertical and horizontal moving equipment, including associated electrical equipment and builders work.
Special Services.
Special services, including associated electrical work and builders work. Includes gas, liquids, fume extraction systems, pneumatic and vacuum tube systems, refrigeration, disposal systems, kitchen, bar and laboratory equipment and fittings, communication systems, protective systems (excluding fire), building management systems, traffic control systems.
Drainage.
Sub-soil drainage, land drains, stormwater drains and soil drains, including excavation, backfill, fittings and the like.
External Works and Sundries
External Works.
Site works beyond the line of the exterior face of the building structure. Excludes site preparation.
Sundries.
Items not readily classified under other elements, e.g., verandahs, canopies, swimming pools, small isolated structures such as pump houses.

## Slide 7
Page 7
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Summary of Elements: P&G, Margins and Contingencies
P&G, Margins and Contingencies
Margins.
All sums identifiable in a tender to cover the Main Contractor’s Profit and Overhead Costs.
Preliminaries.
Normal Builder's preliminaries, i.e., site establishment, temporary services, site management and personnel, plant, equipment, scaffolding, on-site overheads, notices and fees, indirect costs.
Contingencies.
All contract contingency sums contained in the contract
Preliminaries.
Normal Builder's preliminaries, i.e., site establishment, temporary services, site management and personnel, plant, equipment, scaffolding, on-site overheads, notices and fees, indirect costs.
Margins.
All sums identifiable in a tender to cover the Main Contractor’s Profit and Overhead Costs.
Contract Contingencies.
All contract contingency sums contained in the contract
Other Development Costs.
Items included in a capital cost estimate that are not included in the construction contract scope of works and to be supplied or provided by parties other than the construction contractor.

## Slide 8
Page 8
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E1 Site Preparation
Form and Extent of Elements
E1 Site Preparation
Definition
All work necessary to clear a site of existing structures, trees, etc. to create a suitably benched surface as a working platform and to support adjoining structures
Exclusions
Site retaining walls not attached to the structure. See “E23 External Works”, page 34.
Element Element Unit
1 Site Preparation
Area of lowest floor measured over all external walls in m2 (if relevant, relate also to plot area)
Sub-element Unit
Sub-element
1.01 Demolition
Gross area of demolished building stating number of stories
1.02
Site Clearance
Area cleared in m2
1.03
Bulk excavation including basement excavation
Volume excavated in m3 stating area excavated
1.04
Bulk filling and consolidation
Volume of filling in m3 stating area filled
1.05
Temporary ground retainment
Area of face retained in m2
1.06
Underpinning
Length of wall underpinned in metres stating depth of underpinning
1.07
Supports to existing structure (shoring)
Length of wall supported in metres stating height of shoring
1.08
Diversion /termination of existing services, water courses, etc.
Enumerated
1.09
Dewatering
Sum

## Slide 9
Page 9
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E2 Substructure
E2 Substructure
Definition
All work below the underside of the lowest floor finish including all work applicable to the foundations, hardfilling beneath the floor slab, concrete floor slabs, service ducts, lift pits and the like in or beneath the floor slab and hollow timber floor construction.
Where the lowest floor finish varies throughout the building then this element shall contain all work in the various lowest floors and beneath, including basement walls between the different levels. See sketch.
Exclusions
Excavations above the lowest floor level, i.e., basement excavation. See “E1 Site Preparation”, page 8.
Plumbing, drainage or any other services below the lowest floor finish
Site preparation items. See “E1 Site Preparation”, page 8.
Recesses for matwells. See “E12 Floor Finishes”, page 21.
Upstands and machine bases cast onto floor slab. See Elements 4, 7, 8, 10, 15, 16, 17 and 21 as appropriate.
Notes
Excavation shall include backfilling, disposal of surplus and planking and strutting.
Element Element Unit
2 Substructure
Area of lowest floor in m2, measured over exterior walls
Sub-element Unit
Sub-element
2.01 Piling
Total length of all piles in metres stating number, section and type
2.02
Belling of piles
Enumerated
2.03
Strip foundations, including excavation, concrete, formwork and reinforcement
Length of foundation in metres stating sectional dimensions
2.04
Isolated base foundations, including excavation, concrete, formwork and reinforcement
Enumerated stating dimensions
2.05
Concrete in floor slabs on grade, including reinforcement, hardfilling and damp proof membrane
Area of floor slab in m2 stating thickness
2.06
Additional filling under floor slabs
Volume in m3

## Slide 10
Page 10
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E2 Substructure
2.07
Suspended concrete floor slabs, including reinforcement, formwork, propping and topping as appropriate
Area of floor slab in m2 stating thickness
2.08
Underslab service ducts, including excavation, concrete, formwork, reinforcement and duct covers
Length of duct in metres stating sectional dimensions
2.09
Lift and escalator pits, including excavation, concrete, formwork and reinforcement
Enumerated stating number of lifts or escalators
2.10
Tanking, including protection
Area of tanking in m2 stating whether horizontal, sloping or vertical
2.11
Timber floor construction, including flooring, framing, foundation blocks, membranes and insulation
Area of timber floor in m2
2.12
Bulk filling around basement walls
Volume of filling in m3
2.13
Permanent ground retainment
Area of face retained in m2
Element
Element Unit

## Slide 11
Page 11
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E3 Frame
E3 Frame
Definition
All load bearing column and beam framework above lowest floor finish
Major roof framing members such as rafters, joists, etc.
Exclusions
All profiled finishes. See “E13 Wall Finishes”, page 22. See “E14 Ceiling Finishes”, page 23.
All applied finishes. See “E13 Wall Finishes”, page 22. See “E14 Ceiling Finishes”, page 23.
Element Element Unit
3 Frame Gross floor area in m2
Sub-element Sub-element Unit
3.01
Concrete columns, including reinforcement, formwork and fairface finish
Length of member in metres stating sectional dimensions
3.02
Concrete beams, including reinforcement, formwork and fairface finish
Length of member in metres stating sectional dimensions
3.03
Precast concrete columns, including reinforcement, formwork, concrete filling, grouting, etc.
Length of member in metres stating sectional dimensions
3.04
Precast concrete beams, including reinforcement, formwork, concrete filling, grouting, etc.
Length of member in metres stating sectional dimensions
3.05
Structural steel in columns
Weight of steel in tonnes/kilograms
3.06
Structural steel in beams
Weight of steel in tonnes/kilograms
3.07
Timber posts and associated metalwork
Length of members in metres stating sectional dimensions
3.08
Timber beams and associated metalwork
Length of members in metres stating sectional dimensions
3.09
Timber portal frames and associated metalwork
Number stating span and pitch
3.10
Steel portal frames and associated metalwork
Number stating span and pitch
3.11
Timber trusses
Number stating span and pitch
3.12
Steel trusses
Weight of steel in tonnes/kilograms stating span
3.13
Reinforced brick masonry columns
Length of columns in metres stating sectional dimensions
3.14
Reinforced concrete masonry columns
Length of columns in metres stating sectional dimensions
3.15
Reinforced concrete masonry beams
Length of beams in metres stating sectional dimensions

## Slide 12
Page 12
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E3 Frame
3.16
Timber roof frame members
Horizontal area of roof supported in m2 stating pitch
3.17
Steel roof frame members
Weight of steel in tonnes/kilograms stating pitch and horizontal area of roof supported in m2
3.18
Fireproofing of steel frame members
Area covered in m2
Element
Element Unit

## Slide 13
Page 13
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E4 Structural Walls
E4 Structural Walls
Definition
Load bearing and diaphragm walls together with integral columns.
Exclusions
Non structural spandrel panels. See “E7 Exterior Walls and Exterior Finish”, page 16.
Linings and applied finishes or treatments. See “E13 Wall Finishes”, page 22.
Profiled finish. See “E13 Wall Finishes”, page 22.
Element Element Unit
4 Structural Walls Total area of structural walls in m2
Sub-element Sub-element Unit
4.01
Concrete walls, including reinforcement, formwork and fairface finish
Area in m2 for each type of wall stating thickness
4.02
Reinforced concrete masonry walls, including reinforcement, formwork, concrete filling, grouting, etc.
Area in m2 for each type of wall stating thickness

## Slide 14
Page 14
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E5 Upper Floors
E5 Upper Floors
Definition
Suspended floors, mezzanine floors, balcony floors and roof slabs.
Exclusions
Floor support beams. See “E3 Frame”, page 11.
Soffit treatments. See “E14 Ceiling Finishes”, page 23.
Element Element Unit
5 Upper Floors Total area of upper floors in m2
Sub-element Sub-element Unit
5.01 Timber floors including flooring
Area in m2 for each type of floor stating thickness or overall depth
5.02
Concrete floors and/or roof slabs, including reinforcement, formwork and fairface finish
Area in m2 for each type of floor stating thickness or overall depth
5.03
Proprietary type floors, including reinforcement, formwork and concrete topping
Area in m2 for each type of floor stating thickness or overall depth

## Slide 15
Page 15
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E6 Roof
E6 Roof
Definition
Complete weatherproof covering of all types to roofs.
Roofs are deemed to include decks, a deck being defined as having habitable space beneath and no structure above.
Diaphragm bracing, sarking and screeds
Exclusions
All support beams, joists, trusses and rafters. See “E3 Frame”, page 11.
All insitu or precast concrete roof slabs. See “E5 Upper Floors”, page 14.
Parapets and finishes to parapets. See “E7 Exterior Walls and Exterior Finish”, page 16.
Gables and gable finishes. See “E7 Exterior Walls and Exterior Finish”, page 16.
Canopies, balconies, covered ways and verandahs. Balconies are deemed to be projections beyond the face of the structure. See “E24 Sundries”, page 35.
Roof top structures housing water supply tanks, lift motor rooms, etc. See respective elements.
Element Element Unit
6 Roof Horizontal area of roof in m2
Sub-element Sub-element Unit
6.01 Roof covering and associated flashings
Area of covering in m2 (measured on the slope) for each type of covering
6.02
Deck covering and associated flashings
Area of covering in m2 (measured on the slope) for each type of covering
6.03
Roof support components, such as roof purlins, tile battens, diaphragm bracing, sarking and screeds
Area of roof support systems in m2 (measured on the slope) for each type
6.04
Thermal or acoustic insulation to underside of roof covering
Area of insulation in m2
6.05
Verge facing and soffits, including supporting framing
Length of verge in metres stating width
6.06
Eaves facing and soffits, including supporting framing
Length of eaves in metres stating width
6.07
Secret or parapet gutters, including supporting framing
Length of gutter in metres
6.08
Eaves gutters
Length of gutter in metres
6.09
Downpipes
Length of downpipe in metres
6.10
Roof lights, including frames, upstands, flashings and linings
Area of rooflighting in m2, or enumerated as appropriate
6.11
Translucent sheeting
Area of translucent roofing in m2, or enumerated as appropriate

## Slide 16
Page 16
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E7 Exterior Walls and Exterior Finish
E7 Exterior Walls and Exterior Finish
Definition
All work to exterior walls, including applied or insitu finishes
Includes gable ends, parapets, spandrels and finishes. Includes both skins of exterior cavity walls together with any exterior finish. Includes applied exterior finishes to exterior columns, beams and structural spandrels and walls.
Exclusions
Curtain walls. See “E8 Windows and Exterior Doors”, page 17.
Element Element Unit
7 Exterior Walls and Exterior Finish Wall area in m2
Sub-element Sub-element Unit
7.01
Concrete walls, including reinforcement, formwork and surface finishes
Area in m2 for each type of wall stating thickness
7.02
Concrete spandrels and parapets, including reinforcement, formwork and surface finishes
Area in m2 for each type of spandrel or parapet stating thickness
7.03
Precast concrete wall panels, including integral finishes
Area in m2 for each type stating thickness
7.04
Precast concrete spandrel/parapet panels
Area in m2 for each type stating thickness
7.05
Timber wall framing
Area in m2 for each type stating thickness
7.06
Brick walls
Area in m2 for each type stating thickness
7.07
Concrete masonry walls
Area in m2 for each type stating thickness
7.08
Steel or metal wall framing
Area in m2 stating components and spacings
7.09
Cladding and/or applied finish to exterior faces of structural walls, non-structural walls, columns, beams spandrels and parapets
Area in m2 for each type of finish
7.10
Girts to metal or similar cladding
Area in m2 of cladding supported stating spacing of girts
7.11
Nibs, kerbs and upstands
Length in metres stating dimensions

## Slide 17
Page 17
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E8 Windows and Exterior Doors
E8 Windows and Exterior Doors
Definition
All windows and doors in exterior walls including vertical or near vertical glazing
Exclusions
Rooflights. See “E6 Roof”, page 15.
Interior glazed screens. See “E10 Interior Walls”, page 19. See “E11 Interior Doors”, page 20.
Curtain pelmets. See “E15 Fittings and Fixtures”, page 24.
Sun screens. See “E24 Sundries”, page 35.
Curtains, tracks and blinds. See “E24 Sundries”, page 35.
Element Element Unit
8 Windows and Exterior Doors Area of windows and exterior doors in m2
Sub-element Sub-element Unit
8.01
Aluminium, steel and timber windows, including frames and sills, weatherbars, glazing, fixing, special rebates, pointing, paint, hardware, fixing lugs or pockets, flashings, facings and trim, opening gear and the like
Area in m2 (excluding door openings) for each type
8.02
Shop fronts, including frames and sills, weatherbars, glazing, fixing, special rebates, pointing, paint, hardware, fixing lugs or pockets, flashings, facings and trim, opening gear and the like
Area in m2 (excluding door openings) staying type
8.03
Curtain walling, including glass
Area in m2 (excluding door openings)
8.04
Aluminium, steel, timber and glass doors, including glazing, fixing, painting, hardware and the like, where an integral component of 8.01,
8.02 or 8.03 above.
Enumerated for each type
8.05
Isolated doors and frames, including frames and sills, weatherbars, glazing, fixing, special rebates, pointing, paint, hardware, fixing lugs or pockets, flashings, facings and trim, opening gear and the like
Enumerated for each type
8.06
Roller shutter, folding or tilt doors, complete with all trim, fixings, special supports and the like
Enumerated stating size

## Slide 18
Page 18
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E9 Stairs and Balustrades
E9 Stairs and Balustrades
Definition
Flights and intermediate landings including integral finishings, handrails and balustrades
Exclusions
Applied finishes. See “E12 Floor Finishes”, page 21. See “E14 Ceiling Finishes”, page 23.
Element Element Unit
9 Stairs and Balustrades Gross floor area in m2
Sub-element Sub-element Unit
9.01 Stairs
Area in m2 (metres rise x metres width) of each type of stair
9.02
Handrails
Length in metres for each type
9.03
Balustrades
Length of balustrade in metres stating the height and type
9.04
Cat ladders and cat walks
Length in metres

## Slide 19
Page 19
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E10 Interior Walls
E10 Interior Walls
Definition
All interior walls, including glazed screens, proprietary partitions and sound/fire rated walls.
Exclusions
Fanlights and sidelights. See “E11 Interior Doors”, page 20.
Folding or sliding doors forming partitions. See “E11 Interior Doors”, page 20.
Wall finishes. See “E13 Wall Finishes”, page 22.
Element Element Unit
10 Interior Walls Area of interior walls in m2
Sub-element Sub-element Unit
10.01 Timber framed partitions, excluding linings
Area in m2 (excluding door openings) stating details
10.02
Steel framed partitions, excluding linings
Area in m2 (excluding door openings) stating details
10.03
Glazed screens, including glass and finish, but excluding doors
Area in m2 (excluding door openings) stating details
10.04
Proprietary partition systems, including linings and finishings
Area in m2 (excluding door openings) stating details
10.05
Steel mesh screens, including framework and netting
Area in m2 (excluding door openings) stating details
10.06
Concrete, concrete masonry, brick and other types of masonry partition walls, excluding finishings
Area in m2 (excluding door openings) stating details
10.07
Interior shop fronts
Area in m2 (excluding door openings) stating details
10.08
Nibs, kerbs and upstands
Length in metres stating dimensions
10.09
Proprietary toilet and shower cubicles, including linings, doors, finishing and hardware
Enumerated for each cubicle

## Slide 20
Page 20
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E11 Interior Doors
E11 Interior Doors
Definition
All interior doors, including frames, architraves, finishes, glazing, fanlights, side lights, panels over doors, hardware and control systems.
Exclusions
Doors to proprietary partition systems. See “E10 Interior Walls”, page 19.
Doors to fittings and fixtures. See “E15 Fittings and Fixtures”, page 24.
Element Element Unit
11 Interior Doors Number of doors giving area in m2
Sub-element Sub-element Unit
11.01 | Timber doors | Enumerated for each type stating size
11.02 | Metal doors | Enumerated for each type stating size
11.03 | Doors with fanlights and/or sidelights | Enumerated for each type stating size
11.04 | Doors with panels over | Enumerated for each type stating size
11.05 | Folding or sliding doors | Enumerated for each type stating size
11.06 | Operable walls | Enumerated for each type stating size
11.07 | Fire rated doorsets | Enumerated for each type stating size
11.08 | Strongroom doors/grilles | Enumerated for each type stating size
11.09 | Roller shutters | Enumerated for each type stating size
11.10 | Wall hatches | Enumerated for each type stating size
11.11 | Duct doors | Enumerated for each type stating size

## Slide 21
Page 21
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E12 Floor Finishes
E12 Floor Finishes
Definition
Includes all preparatory work, screeds, surface finishes, matwells and threshold strips.
Raised floors laid over structural floors.
Element Element Unit
12 Floor Finishes Total area of floor finishes in m2
Sub-element Sub-element Unit
12.01 Floor finishes and coverings Area in m2 for each type of finish
12.02
Floor finishes and coverings to stairs and Area in m2 for each type of finish intermediate landings
12.03
Floor screeds
Area in m2 stating thickness or average thickness
12.04
Raised floors complete with bearers laid over structural floors
Area in m2 stating details
12.05
Matwells and mats
Enumerated stating size
12.06
Junction strips, nosings and the like
Length in metres stating details

## Slide 22
Page 22
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E13 Wall Finishes
E13 Wall Finishes
Definition
Includes all preparatory work and finishes to interior walls, isolated columns, and to interior faces of exterior walls.
Exclusions
Fair face finish to concrete. See “E3 Frame”, page 11. See “E4 Structural Walls”, page 13.
Finishes to proprietary partition systems and the like. See “E10 Interior Walls”, page 19.
Element Element Unit
Wall Finishes Total area of wall finishes in m2
Sub-element Sub-element Unit
  Wall linings and finishes Area in m2 stating details
  Strapping behind linings Area in m2 stating details
  Insulation behind linings Area in m2 stating details
  Profiled finish to concrete walls or columns Area in m2 stating details
  Column cladding Area in m2 stating details
  Skirtings, cornices, trims, dado rails and the like Length in metres stating details
  Wall access panels Enumerated stating size

## Slide 23
Page 23
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E14 Ceiling Finishes
E14 Ceiling Finishes
Definition
Includes all preparatory work and finishes, suspended ceilings and framing, soffits of staircases and intermediate landings.
Exclusions
Ceiling framing forming part of roof framing. See “E3 Frame”, page 11.
Element Element Unit
Ceiling Finishes Total area of ceiling finishes in m2
Sub-element Sub-element Unit
  Ceiling linings and finishes Area of each type in m2
  Beam cladding Area of each type in m2
  Ceiling framing Area of each type in m2
  Strapping behind linings Area of each type in m2
  Insulation behind linings Area of each type in m2
14.06
14.07
14.08
14.09
Proprietary suspended ceilings, including Area of each type in m2 ceiling finish
Mouldings, cover battens and the like Length in metres stating details
Isolated in-ceiling fire and sound baffles, Area in m2 stating details including framing
Ceiling access panels and ceiling features Enumerated stating size

## Slide 24
Page 24
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E15 Fittings and Fixtures
E15 Fittings and Fixtures
Definition
Built-in joinery fittings or joinery fittings fixed in position, including glass, hardware and finishes.
Exclusions
Sanitary fittings. See “E16 Sanitary Plumbing”, page 25.
Electrical fittings. See “E19 Electrical Services”, page 29.
Services to fittings and fixtures. See respective elements.
Element Unit
Gross floor area in m2
Element
15 Fittings and Fixtures
Sub-element
Sub-element Unit
15.01 | Wardrobes | Enumerated stating size
15.02 | Cupboards | Enumerated stating size
15.03 | Shelving units | Enumerated stating size
15.04 | Shelving | Length in metres stating width
15.05 | Sink, vanity and bench units | Enumerated stating size
15.06 | Sink, vanity and bench tops | Enumerated stating size
15.07 | Lockers, fixed desks, tables and bunk beds | Enumerated stating size
15.08 | Safes | Enumerated stating details
15.09 | Cloakroom fittings | Enumerated stating details
15.10 | Benches and seating | Enumerated stating details
15.11 | Counters, bars and the like | Enumerated stating details
15.12 | Chalk boards projection screens and notice boards | Enumerated stating details
15.13 | Telephone booths | Enumerated stating details
15.14 | Curtain pelmets | Length in metres
15.15 | Mirrors | Enumerated stating size
15.16 | Storage racks | Area in m2 stating size and details
15.17 | Miscellaneous hardware | Enumerated stating details

## Slide 25
Page 25
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E16 Sanitary Plumbing
E16 Sanitary Plumbing
Definition
Hot and cold water supply, including hot water cylinder, sanitary fittings, soil, waste and vent pipes.
Exclusions
Special kitchen equipment. See “E21 Special Services”, page 32.
Laboratory equipment and services. See “E21 Special Services”, page 32.
Element Element Unit
16 Sanitary Plumbing
Enumerated (i.e. number of sanitary fittings, including sink-benches and vanity units)
Sub-element
Sub-element Unit
16.01
Incoming water supply, including meters, valves, connections and insulation
Length in metres stating size
16.02
Cold water supply pipework to fittings and outlets, including valves and insulation
Number of outlets
16.03
Hot water supply pipework to fittings and outlets, including valves and insulation
Number of outlets
16.04
Hot water cylinders, including associated valves
Enumerated stating details
16.05
Pumps, including associated valves
Enumerated stating details
16.06
Flushing systems
Number of outlets
16.07
Sanitary fittings, sinks and bowls, including associated taps, traps and valves
Number of sanitary fittings stating type of fitting
16.08
Soil, waste, overflow and vent piping to fittings
Number of fittings served
16.09
Storage tanks, including associated valves and restraints/platforms
Enumerated stating details
16.10
Acoustic insulation
Sum
16.11
Permits, testing, identification, 'As Built' drawings and builders work
Sum

## Slide 26
Page 26
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E17 Heating and Ventilation Services
E17 Heating and Ventilation Services
Definition
Heating, ventilation and air conditioning systems, including all associated equipment.
Exclusions
Heating source to hot water system. See “E16 Sanitary Plumbing”, page 25.
Note
Sub-elements for Heating and Ventilation Services should be analyzed according to the type of system as listed under Element below, e.g. a silencer on a ventilation system would be analyzed as sub-element 17.05.08.
Element Element Unit
17 Heating and Ventilation Services
Sub-element
Sub-element Unit
17.01 | Chillers | Enumerated
17.02 | Boilers (including flues, fuel supply and storage tanks, and support equipment) | Enumerated
17.03 | Pumps | Enumerated
17.04 | Cooling towers | Enumerated
17.05 | Fresh air supply units | Enumerated
17.06 | Variable speed drives | Enumerated
17.07 | Air Handling Units | Enumerated
17.08 | Silencers | Enumerated
17.09 | Fan Coil Units | Enumerated
17.10 | Hydronic Units | Enumerated
17.11 | VAV Terminal Units | Enumerated
17.12 | Ventilation Fans | Enumerated
17.13 | Unitary Packaged Air Conditioners | Enumerated

## Slide 27
Page 27
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E17 Heating and Ventilation Services
}
}
}
percentage of the cost of the system
Element |  |  | Element Unit
17.14 | Condensing Units |  | Enumerated
17.15 | Air Cooled Condensers |  | Enumerated
17.16 | Air Cooled Water Coolers |  | Enumerated
17.17 | Ceiling Diffusers, complete with flexible duct, diffuser boot and damper |  | Enumerated
17.18 | Extract Grilles |  | Enumerated
17.19 | Ductwork, including fire dampers |  | Surface area of duct in m2
17.20 | Acoustic Duct Lining |  | Surface area of duct in m2 stating thickness
17.21 | External Duct Insulation |  | Surface area of duct in m2 stating thickness
17.22 | Kitchen Hoods |  | Enumerated stating dimensions
17.23 | Radiators/Heating units |  | Enumerated
17.24 | Controls (using a BMS/without a BMS)} | } | 
17.25 | Electrical, including switchboards and control | } } | 
 | panels | } } Gross area of building served for each type of | 
17.26 | Pipework | } system. May also be expressed as a | 
17.27 | Pipework Insulation } |  | 
17.28
Commissioning and testing
17.29
Permits, Servicing (during defects liability period), Sundries, Identification, Preliminary and General, Profit and Overhead
Sum
17.30
Builders Work
Sum

## Slide 28
Page 28
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E18 Fire Services
E18 Fire Services
Definition
All fire services within a building, including all associated electrical work.
Element Element Unit
18 Fire Services Gross floor area in m2
Sub-element Sub-element Unit
18.01
18.02
18.03
18.04
18.05
18.06
18.07
18.08
18.09
18.10
18.11
18.12
18.13
Incoming water supply, including meters, valves Length in metres stating size and connections
Water storage tanks, including associated Enumerated stating details valves
Pipework, valves, pumps and equipment within Sum sprinkler valve room
Sprinkler installation (outside of sprinkler valve Number of sprinkler heads room)
Smoke detector installation Number of detector heads
Heat detector installation Number of detector heads
Manual call systems Number of bell stations
Dry riser installation Number of floor levels served
Wet riser installation Number of floor levels served
Hydrant mains Number of hydrants served
Hose reels, including associated supply Enumerated pipework
Extinguishers and the like Enumerated
Permits, testing, identification, 'As Built' Sum drawings and builders work

## Slide 29
Page 29
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E19 Electrical Services
E19 Electrical Services
Definition
All electrical services providing lighting and power.
Exclusions
Lighting and power to external works. See “E23 External Works”, page 34.
Wiring to equipment and machinery which is covered in other elements.
Element Element Unit
19 Electrical Services Gross floor area in m2
Sub-element Sub-element Unit
19.01 Transformers Enumerated stating details
19.02
19.03
19.04
19.05
Incoming mains cables, including trenching, Length in metres stating cable size cable ducts and cable covers, where applicable
Main switchboard Enumerated stating details
Sub-main cables, including trenching, cable Length in metres stating cable size ducts and cable covers, where applicable
Distribution boards Enumerated stating details
19.06
Circuit wiring to lighting outlets, including switches
Number of outlets and switches stating the system employed (i.e. conventional, harness, etc.)
19.07
Circuit wiring to power outlets, including outlet fittings
Number of outlets and switches stating the system employed (i.e. conventional, harness, etc.)
19.08
Circuit wiring to shaver outlets, including outlet fittings
Number of outlets
19.09
Circuit wiring to fixed wired outlets, e.g. stoves, HWC’s, heaters, etc.
Number of outlets
19.10
Circuit wiring to single phase equipment and machinery outlets
Number of outlets
19.11
Circuit wiring to three phase equipment and machinery outlets
Number of outlets
19.12
Trunking, cable trays and ladders
Length in metres stating details
19.13
Light fittings
Enumerated stating type
19.14
Lighting control panels
Enumerated
19.15
Dimmers
Enumerated
19.16
Clock systems
Number of clocks
19.17
Emergency lighting systems
Number of light outlets

## Slide 30
Page 30
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E19 Electrical Services
Element |  | Element Unit
19.18 | Specialist lighting | Sum
19.19 | Earthing and bonding | Sum
19.20 | Permits, testing, identification, ‘As Built’ drawings, manuals and builders work | Sum

## Slide 31
Page 31
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E20 Vertical and Horizontal Transportation
E20 Vertical and Horizontal Transportation
Definition
Vertical and horizontal moving equipment, including associated electrical equipment and builders work.
Element Element Unit
20 Vertical and Horizontal Transportation Gross floor area in m2
Sub-element Sub-element Unit
20.01 Passenger lifts
Enumerated giving description of each type of equipment stating number of floors served, speed and method of control
20.02
Goods lifts
Enumerated giving description of each type of equipment stating number of floors served, speed and method of control
20.03
Dumb waiters
Enumerated giving description of each type of equipment stating number of floors served, speed and method of control
20.04
Passenger escalators, travellators, goods escalators and conveyors
Enumerated giving description of each type of equipment
20.05
Gantry cranes, including support structures, e.g. rails and corbels
Enumerated giving description of each type of equipment
20.06
Hoists
Enumerated giving description of each type of equipment
20.07
Building maintenance units
Enumerated giving description of each type of equipment
20.08
Permits, testing, identification, ‘As Built’ drawings, and maintenance manuals
Sum
20.09
Builders work
Sum

## Slide 32
Page 32
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E21 Special Services
E21 Special Services
Definition
Special services, including associated electrical work and builders work.
Element Element Unit
21 Special Services Gross floor area in m2
Sub-element Sub-element Unit
21.01 Gases and compressed air services Number of outlets or fittings
21.02
21.03
21.04
21.05
21.06
21.07
21.08
21.09
21.10
21.11
21.12
Liquids of various types (supply and waste Number of outlets or fittings systems)
Fume extraction systems Number of outlets or fittings
Pneumatic and vacuum tube systems Number of outlets or fittings
Local refrigeration and cool room installations Enumerated, describing extent of each system
Sanitary and refuse incinerator and disposal Enumerated, describing extent of each system systems, including waste disposal units
Specialist kitchen equipment, including hoods, Enumerated, describing extent of each system ducts and fans
Specialist laboratory equipment Enumerated, describing extent of each system
Communication systems Enumerated, describing extent of each system
Internal call systems
Telephone systems
Radio and TV systems
Data networks
Protective systems (excluding fire) Enumerated, describing extent of each system
Security systems
Lightning conductor systems
Emergency staged evacuation systems
Building management systems Enumerated, describing extent of each system
Traffic control systems Enumerated, describing extent of each system
21.13
Stoves, refrigerators, washing machines, dryers, bottle coolers, ice makers, glass and dish washing machines, etc.
Enumerated, describing extent of each system
21.14
Permits, testing, identification, ‘As Built’ drawings, commissioning, manuals and builders work
Sum

## Slide 33
Page 33
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E22 Drainage
E22 Drainage
Definition
Sub-soil drainage, land drains, stormwater drains and soil drains, including excavation, backfill, fittings and the like.
Element Element Unit
22 Drainage Gross floor area in m2
Sub-element Sub-element Unit
22.01 | Stormwater drains | Length in metres stating size
22.02 | Soil drains | Length in metres stating size
22.03 | Land drains | Length in metres stating size
22.04 | Chemical drains | Length in metres stating size
22.05 | Culverts | Length in metres stating size
22.06 | Stormwater outfalls | Length in metres stating size
22.07 | Channels and gratings | Length in metres stating size
22.08 | Cesspits and grease traps | Enumerated
22.09 | Inspection chambers | Enumerated
22.10 | Manholes | Enumerated
22.11 | Soakholes | Enumerated
22.12 | Holding tanks | Enumerated
22.13 | Pumps | Enumerated
22.14 | Septic tanks | Enumerated
22.15 | Sewage treatment plants | Enumerated
22.16 | Permits, testing, identification, ‘As Built’ drawings and builders work | Sum

## Slide 34
Page 34
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E23 External Works
E23 External Works
Definition
Site works beyond the line of the exterior face of the building structure.
Exclusions
Site preparation. See “E1 Site Preparation”, page 8.
Element Element Unit
23 External Works
Gross area of site in m2, excluding plan area of building
Sub-element
Sub-element Unit
23.01 | Roads | Area in m2
23.02 | Kerbing and channelling | Length in metres
23.03 | Paths, terraces and paved areas | Area in m2 for each type
23.04 | Site retaining walls | Length in metres for each type stating height of ground retained
23.05 | Steps | Enumerated for each flight
23.06 | Screen walls and fencing | Length in metres for each type stating height
23.07 | Flower boxes and planters | Enumerated stating details
23.08 | Grading, seeding and planting | Area in m2
23.09 | Irrigation systems | Area to be irrigated in m2
23.10 | Seats, furniture and the like | Enumerated stating details
23.11 | Pavement cross-overs | Enumerated stating details
23.12 | Plumbing services associated with this element | Respective sub-element units
23.13 | Electrical services associated with this element | Respective sub-element units
23.14 | Security systems associated with this element | Respective sub-element units

## Slide 35
Page 35
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E24 Sundries
E24 Sundries
Definition
Items which do not readily lend themselves to inclusion in other standardised elements due to their singular character.
Element Element Unit
24 Sundries Gross floor area in m2
Sub-element Sub-element Unit
24.01 | Verandahs | Relevant sub-element unit stating details
24.02 | Covered ways | Relevant sub-element unit stating details
24.03 | Sun screens | Relevant sub-element unit stating details
24.04 | Canopies | Enumerated stating details
24.05 | Balconies | Enumerated stating details
24.06 | Sculptures and Artwork | Enumerated stating details
24.07 | Murals and Plaques | Enumerated stating details
24.08 | Signs and lettering | Enumerated stating details
24.09 | Flagpoles | Enumerated stating details
24.10 | Swimming pools | Enumerated stating details
24.11 | Curtains and blinds | Length in metres stating drop and type
24.12 | Curtain tracks | Length in metres stating details
24.13 | Sundry minor alteration work | Sum stating details
24.14 | Small isolated structures such as pump houses, transformer enclosures and the like | Enumerated stating details

## Slide 36
Page 36
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E25 Preliminaries
E25 Preliminaries
Definition
All usual preliminary and general items.
Exclusions
Contingency Sum. See “E27 Contract Contingencies”, page 38.
Element Element Unit
25 Preliminaries Gross floor area in m2
E25 expressed as a percentage value of the sum of elements E1 - E24 inclusive
Sub-element
Sub-element Unit
25.01 | Site establishment | Sum or percentage of total element cost
25.02 | Temporary services | Sum or percentage of total element cost
25.03 | Site management and personnel | Sum or percentage of total element cost
25.04 | Plant and equipment | Sum or percentage of total element cost
25.05 | Scaffolding | Sum or percentage of total element cost
25.06 | Cranage | Sum or percentage of total element cost
25.07 | Hoardings | Sum or percentage of total element cost
25.08 | Messing, ablutions and site accommodation | Sum or percentage of total element cost
25.09 | On-site overheads | Sum or percentage of total element cost
25.10 | Indirect costs | Sum or percentage of total element cost

## Slide 37
Page 37
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E26 Margins
E26 Margins
Definition
All sums identifiable in a tender to cover cost contributions to the Main Contractor’s Profit and Overhead Costs. Where not identifiable, this element is to be noted accordingly.
Element Element Unit
26 Margins Gross floor area in m2
E26 expressed as a percentage value of the sum of elements E1 - E25 inclusive

## Slide 38
Page 38
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
NZIQS Elemental Analysis
Form and Extent of Elements: E27 Contract Contingencies
E27 Contract Contingencies
Definition
All contract contingency sums contained in the contract.
Exclusions
Contingency Sums allocated to a specific purpose not yet detailed. Such sums should be allocated to the element that their specific purpose identifies.
Element Element Unit
27 Contract Contingencies Gross floor area in m2
E27 expressed as a percentage value of the sum of elements E1 - E26 inclusive

## Slide 39
Page 39
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
E27 Contract Contingencies
Definition
• All contract contingency sums contained in the contract.
Exclusions
• Contingency Sums allocated to a specific purpose not yet detailed. Such sums should be allocated to the element that their specific purpose identifies.
Element Element Unit
27 Contract Contingencies Gross floor area in m2
E27 expressed as a percentage value of the sum of elements E1 - E26 inclusive
Element
Element Unit
28
Other Development Costs
Gross floor area in m2
Sub-element
Sub-element Unit
28.01 | Professional fees and disbursements | Sum stating details
28.02 | Direct contracts | Sum stating details
28.03 | Loose furniture and equipment | Sum stating details
28.04 | Client supplied materials | Sum stating details
28.05 | Territorial authority approval or consent fees | Sum stating details
28.06 | Resource consent fees | Sum stating details
28.07 | Development contributions | Sum stating details
28.08 | Temporary accommodation | Sum stating details
28.09 | Removal or relocation costs | Sum stating details
28.10 | Marketing and sales costs | Sum stating details
28.11 | Legal fees | Sum stating details
28.12 | Tenant fit-out contributions | Sum stating details
28.13 | Land acquisition costs | Sum stating details
28.14 | Principal’s bond | Sum stating details
28.15 | Operator licenses | Sum stating details
28.16 | Development management fees and administration costs | Sum stating details
28.17 | Finance and funding costs | Sum stating details
NZIQS Elemental Analysis
Form and Extent of Elements: E28 Other Development Costs
E28 Other Development Costs
Definition
Items included in a capital cost estimate that are not included in the construction contract scope of work and to be supplied or provided by parties other than the construction contractor. These items do not ordi- narily incur contractors’ overhead costs or margins.
Exclusions
On-going asset operating and financing costs
Work mentioned elsewhere within the document

## Slide 40
Page 40
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
Standard Forms
NZIQS Elemental Analysis
Standard Forms: E27 Contract Contingencies

## Slide 41
Page 41
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
External Works and Sundries: 23-24
Preliminaries, Margins, Contingencies: 25-27
NZIQS Elemental Analysis
Standard Forms: Project Summary
Project Summary
Reference:
Number of Stories:
Date of Tender:
Project: |  |  |  | 
Location: |  |  |  | 
Contract Amount: $ | Cost per M2: $ |  | Reference: | 
Tender Range: |  |  | Type of Contract: | 
Gross Floor Area: | Number of Stories: |  | Date of Tender: | 
Net Lettable Area: | Wall/Floor Ratio: |  | Cost Index Reference Series Used: Index No: | 
Brief Description: |  |  |  | 
Brief Cost Summary |  |  |  | 
Element Groups |  | % of Total | Cost per M2 | Total Cost
Structure: 1-5 Exterior Fabric: 6-8 Interior Finishing: 9-15 Services: 16-22 External Works and Sundries: 23-24 Preliminaries, Margins, Contingencies: 25-27 Other Development Costs: 28 |  |  |  | 
Totals |  |  |  | 

## Slide 42
Page 42
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
Project Analysis
Element
Quantity
Unit
Totals
NZIQS Elemental Analysis
Standard Forms: Project Analysis
Gross Floor Area: |  |  | Tender Date: |  | 
Element | Quantity | Unit | Element Unit Rate | Elemental Cost | Total Cost of Element
 | a |  | b=d/a | c=d/GFA | d
Site Preparation Substructure Frame Structural Walls Upper Floors Roof Exterior Walls & Exterior Finish Windows & Exterior Doors Stairs & Balustrades Interior Walls Interior Doors Floor Finishes Wall Finishes Ceiling Finishes Fittings & Fixtures Sanitary Plumbing Heating and Ventilation Services Fire Services Electrical Services Vertical & Horizontal Transportation Special Services Drainage External Works Other Development Costs |  |  |  |  | 
Totals |  |  |  |  | 

## Slide 43
Page 43
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
Element Unit Rate Record Sheet
Description
Quantit
y
Unit
NZIQS Elemental Analysis
Standard Forms: Element Unit Rate Record Sheet
Project: |  |  |  |  | Element No:
Element Title: |  |  |  |  | 
Tender Date: |  | Margin Included in Element Cost: Yes/No |  |  | 
Description | Quantity | Unit | Element Unit Rate | Elemental Cost | Total Cost of Element
 | a |  | b=d/a | c=d/GFA | d
Job No: |  |  |  | Page No: | 

## Slide 44
Page 44
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
List of Groups, Elements, Sub-elements
m2
m2
m2 m2 m2
m2 No
m2 m2
m2
m3 m3 m2
m
m
m3
S02.06 S02.07
membrane
Additional filling under floor slabs
Suspended concrete floor slabs, including reinforcement, formwork, propping and topping as appropriate
NZIQS Elemental Analysis
List of Groups, Elements, Sub-elements: Element Unit Rate Record Sheet
Heading
Unit
m2
m3 m2
Code GP_A GP_B GP_C | Description Structure Exterior Fabric Interior Finishing | Heading Unit m2 m2 m2
GP_D | Services | m2
GP_E | External Works and Sundries | m2
GP_F | Preliminaries Margins and Contingencies | m2
EL01 | Site Preparation | m2
EL02 | Substructure | m2
EL03 | Frame | m2
EL04 | Structural Walls | m2
EL05 | Upper Floors | m2
EL06 | Roof | m2
EL07 | Exterior Walls & Exterior Finish | m2
EL08 | Windows & Exterior Doors | m2
EL09 | Stairs & Balustrades | m2
EL10 | Interior Walls | m2
EL11 | Interior Doors | No
EL12 | Floor Finishes | m2
EL13 | Wall Finishes | m2
EL14 | Ceiling Finishes | m2
EL15 | Fittings & Fixtures | m2
EL16 | Sanitary Plumbing | No
EL17 | Heating and Ventilation Services | m2
EL18 | Fire Services | m2
EL19 | Electrical Services | m2
EL20 | Vertical and Horizontal Transportation | m2
EL21 | Special Services | m2
EL22 | Drainage | m2
EL23 | External Works | m2
EL24 | Sundries | m2
EL25 | Preliminaries | m2
EL26 | Margins | m2
EL27 | Contract Contingencies | m2
EL28 | Other Development Costs | m2
S01.01 | Demolition | No
S01.02 | Site Clearance | m2
S01.03 | Bulk excavation including basement excavation | m3
S01.04 | Bulk filling and consolidation | m3
S01.05 | Temporary ground retainment | m2
S01.06 | Underpinning | m
S01.07 | Supports to existing structure (shoring) | m
S01.08 | Diversion /termination of existing services, water courses, etc. | No
S01.09 | Dewatering | Sum
S02.01 | Piling | m
S02.02 | Belling of piles | No
S02.03 | Strip foundations, including excavation, concrete, formwork and reinforcement | m
S02.04 | Isolated base foundations, including excavation, concrete, formwork and reinforcement | No
S02.05 | Concrete in floor slabs on grade, including reinforcement, hardfilling and damp proof | m2

## Slide 45
Page 45
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
S02.08
Underslab service ducts, including excavation, concrete, formwork, reinforcement and duct
covers
Lift and escalator pits, including excavation, concrete, formwork and reinforcement
Tanking, including protection
N
m
S02.09 S02.10 S02.11
Timber floor construction, including flooring, framing, foundation blocks, membranes and
m
m
insulation
Bulk filling around basement walls
Permanent ground retainment
Concrete columns, including reinforcement, formwork and fairface finish Concrete beams, including reinforcement, formwork and fairface finish
etc
S02.12 S02.13 S03.01 S03.02 S03.03 S03.04 S03.05 S03.06 S03.07 S03.08 S03.09 S03.10 S03.11 S03.12 S03.13 S03.14 S03.15 S03.16 S03.17 S03.18 S04.01 S04.02
m
m
o
2
3
2
2
2
S05.01 S05.02 S05.03 S06.01 S06.02 S06.03
Fireproofing of steel frame members
Concrete walls, including reinforcement, formwork and fairface finish
Reinforced concrete masonry walls, including reinforcement, formwork, concrete filling, grouting, etc
Timber floors including flooring
Concrete floors and/or roof slabs, including reinforcement, formwork and fairface finish Proprietary type floors, including reinforcement, formwork and concrete topping
Roof covering and associated flashings Deck covering and flashings
Roof support components, such as roof purlins, tile battens, diaphragm bracing, sarking and screeds
Thermal or acoustic insulation to underside of roof covering
Verge facing and soffits, including supporting framing Eaves facing and soffits, including supporting framing Secret or parapet gutters, including supporting framing Eaves gutters
Downpipes
Roof lights, including frames, upstands, flashings and linings Translucent sheeting
Concrete walls, including reinforcement, formwork and surface finishes
Concrete spandrels and parapets, including reinforcement, formwork and surface finishes
Precast concrete wall panels, including integral finishes Precast concrete spandrel/parapet panels
Timber wall framing Brick walls
Concrete masonry walls Steel or metal wall framing
S06.04 S06.05 S06.06 S06.07 S06.08 S06.09 S06.10 S06.11 S07.01 S07.02 S07.03 S07.04 S07.05 S07.06 S07.07 S07.08 S07.09
S07.10 S07.11
Cladding and/or applied finish to exterior faces of structural walls, non-structural walls, columns, beams spandrels and parapets
Girts to metal or similar cladding
Nibs kerbs and upstands
NZIQS Elemental Analysis
List of Groups, Elements, Sub-elements: Element Unit Rate Record Sheet
Precast concrete columns, including reinforcement, formwork, concrete filling, grouting, etc. Precast concrete beams, including reinforcement, formwork, concrete filling, grouting, etc. Structural steel in columns
Structural steel in beams
Timber posts and associated metalwork Timber beams and associated metalwork
Timber portal frames and associated metalwork Steel portal frames and associated metalwork Timber trusses
Steel trusses
Reinforced brick masonry columns Reinforced concrete masonry columns Reinforced concrete masonry beams Timber roof frame members
Steel roof frame members
m
No m2 m2
.m
m
m2 m2 m2 m2 m2 m2
m2 m m m m m m2 m2 m2 m2 m2 m2 m2 m2 m2 m2 m2
m2 m2
m3 m2 m m m m
tonne tonne m
m No No No
tonne m
m m m2
tonne m2 m2 m2

## Slide 46
Page 46
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
S08.01
S08.02
S08.03 S08.04
S08.05
S08.06
Aluminium, steel and timber windows, including frames and sills, weatherbars, glazing, fixing, special rebates, pointing, paint, hardware, fixing lugs or pockets, flashings, facings and trim, opening gear and the like
Shop fronts, including frames and sills, weatherbars, glazing, fixing, special rebates,
pointing, paint, hardware, fixing lugs or pockets, flashings, facings and trim, opening gear and the like
Curtain walling, including glass
Aluminium, steel, timber and glass doors, including glazing, fixing, painting, and the like, where an integral component of 8.01, 8.02 or 8.03 above.
Isolated doors and frames, including frames and sills, weatherbars, glazing, fixing, special
rebates, pointing, paint, hardware, fixing lugs or pockets, flashings, facings and trim, opening gear and the like
Roller shutter, folding or tilt doors, complete with all trim, fixings, special supports and the
No
NZIQS Elemental Analysis
List of Groups, Elements, Sub-elements: Element Unit Rate Record Sheet
 | like | 
S09.01 | Stairs | m2
S09.02 | Handrails | m
S09.03 | Balustrades | m
S09.04 | Cat ladders and cat walks | m
S10.01 | Timber framed partitions, excluding linings | m2
S10.02 | Steel framed partitions, excluding linings | m2
S10.03 | Glazed screens, including glass and finish but excluding doors | m2
S10.04 | Proprietary partition systems, including linings and finishings | m2
S10.05 | Steel mesh screens, including framework and netting | m2
S10.06 | Concrete, concrete masonry, brick and other types of masonry partition walls, excluding | m2
 | finishings | 
S10.07 | Interior shop fronts | m2
S10.08 | Nibs, kerbs and upstands | m
S10.09 | Proprietary toilet and shower cubicles, including linings, doors, finishing and hardware | No
S11.01 | Timber doors | No
S11.02 | Metal doors | No
S11.03 | Doors with fanlights and/or sidelights | No
S11.04 | Doors with panels over | No
S11.05 | Folding or sliding doors | No
S11.06 | Operable walls | No
S11.07 | Fire rated doorsets | No
S11.08 | Strongroom doors/grilles | No
S11.09 | Roller shutters | No
S11.10 | Wall hatches | No
S11.11 | Duct doors | No
S12.01 | Floor finishes and coverings | m2
S12.02 | Floor finishes and coverings to stairs and intermediate landings | m2
S12.03 | Floor screeds | m2
S12.04 | Raised floors complete with bearers laid over structural floors | m2
S12.05 | Matwells and mats | No
S12.06 | Junction strips, nosings and the like | m
S13.01 | Wall linings and finishes | m2
S13.02 | Strapping behind linings | m2
S13.03 | Insulation behind linings | m2
S13.04 | Profiled finish to concrete walls or columns | m2
S13.05 | Column cladding | m2
S13.06 | Skirtings, cornices, trims, dado rails and the like | m
S13.07 | Wall access panels | No
S14.01 | Ceiling finishes and linings | m2
S14.02 | Beam cladding | m2
S14.03 | Ceiling framing | m2
S14.04 | Strapping behind linings | m2
S14.05 | Insulation behind linings | m2
S14.06 | Proprietary suspended ceilings | m2
m2
m2
m2 No
No
No

## Slide 47
Page 47
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
S14.07 S14.08 S14.09 | Mouldings cover battens and the like In-ceiling fire and sound baffles including framing Ceiling access panels | m m2 No
S15.01 | Wardrobes | No
S15.02 | Cupboards | No
S15.03 | Shelving units | No
S15.04 | Shelving | m
S15.05 | Sink, vanity and bench units | No
S15.06 | Sink, vanity and bench tops | No
S15.07 | Lockers, fixed desks, tables and bunk beds | No
S15.08 | Safes | No
S15.09 | Cloakroom fittings | No
S15.10 | Benches and seating | No
S15.11 | Counters, bars and the like | No
S15.12 | Chalk boards projection screens and notice boards | No
S15.13 | Telephone booths | No
S15.14 | Curtain pelmets | m
S15.15 | Mirrors | No
S15.16 | Storage racks | m2
S15.17 | Miscellaneous hardware | No
S16.01 | Incoming water supply, including meters, valves, connections and insulation | m
S16.02 | Cold water supply pipework to fittings and outlets, including valves and insulation | No
S16.03 | Hot water supply pipework to fittings and outlets, including valves and insulation | No
S16.04 | Hot water cylinders, including associated valves | No
S16.05 | Pumps, including associated valves | No
S16.06 | Flushing systems | No
S16.07 | Sanitary fittings, sinks and bowls, including associated taps, traps and valves | No
S16.08 | Soil, waste, overflow and vent piping to fittings | No
S16.09 | Storage tanks, including associated valves and restraints/platforms | No
S16.10 | Acoustic insulation | Sum
S16.11 | Permits, testing, identification, 'As Built' drawings and builders work | Sum
S17.01 | Chillers | No
S17.02 | Boilers, including flues, fuel supply and storage tanks, and support equipment | No
S17.03 | Pumps | No
S17.04 | Cooling towers | No
S17.05 | Fresh air supply units | No
S17.06 | Variable speed drives | No
S17.07 | Air Handling Units | No
S17.08 | Silencers | No
S17.09 | Fan Coil Units | No
S17.10 | Hydronic Units | No
S17.11 | VAV Terminal Units | No
S17.12 | Ventilation Fans | No
S17.13 | Unitary Packaged Air Conditioners | No
S17.14 | Condensing Units | No
S17.15 | Air Cooled Condensers | No
S17.16 | Air Cooled Water Coolers | No
S17.17 | Ceiling Diffusers, complete with flexible duct, diffuser boot and damper | No
S17.18 | Extract Grilles | No
NZIQS Elemental Analysis
List of Groups, Elements, Sub-elements: Element Unit Rate Record Sheet

## Slide 48
Page 48
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
S17.__.19
S17.__.20 S17.__.21 S17.__.22 S17.__.23 S17.__.24 S17.__.25 S17.__.26
S17.__.27
S17.__.28 S17.__.29
S17.__.30
m
NZIQS Elemental Analysis
List of Groups, Elements, Sub-elements: Element Unit Rate Record Sheet
S17 .19 S17 .20 S17 .21 | Ductwork, including fire dampers Acoustic Duct Lining External Duct Insulation | m2 m2 m2
S17 .22 | Kitchen Hoods | No
S17 .23 | Radiators/Heating units | No
S17 .24 | Controls, using a BMS/without a BMS | m2
S17 .25 | Electrical, including switchboards and control panels | m2
S17 .26 | Pipework | m2
S17 .27 | Pipework Insulation | m2
S17 .28 | Commissioning and testing | m2
S17 .29 | Permits, Servicing, during defects liability period, Sundries, Identification, Preliminary and | Sum
 | General, Profit and Overhead | 
S17 .30 | Builders Work | Sum
S18.01 | Incoming water supply, including meters, valves and connections | m
S18.02 | Water storage tanks, including associated valves | No
S18.03 | Pipework, valves, pumps and equipment within sprinkler valve room | Sum
S18.04 | Sprinkler installation, outside sprinkler valve room | No
S18.05 | Smoke detector installation | No
S18.06 | Heat detector installation | No
S18.07 | Manual call systems | No
S18.08 | Dry riser installation | No
S18.09 | Wet riser installation | No
S18.10 | Hydrant mains | No
S18.11 | Hose reels, including associated supply pipework | No
S18.12 | Extinguishers and the like | No
S18.13 | Permits, testing, identification, 'As Built' drawings and builders work | Sum
S19.01 | Transformers | No
S19.02 | Incoming mains cables, including trenching, cable ducts and cable covers, where | m
 | applicable | 
S19.03 | Main switchboard | No
S19.04 | Sub-main cables, including trenching, cable ducts and cable covers, where applicable | m
S19.05 | Distribution boards | No
S19.06 | Circuit wiring to lighting outlets, including switches | No
S19.07 | Circuit wiring to power outlets, including outlet fittings | No
S19.08 | Circuit wiring to shaver outlets, including outlet fittings | No
S19.09 | Circuit wiring to fixed wired outlets, e.g. stoves, HWC’s, heaters, etc. | No
S19.10 | Circuit wiring to single phase equipment and machinery outlets | No
S19.11 | Circuit wiring to three phase equipment and machinery outlets | No
S19.12 | Trunking, cable trays and ladders | m
S19.13 | Light fittings | No
S19.14 | Lighting control panels | No
S19.15 | Dimmers | No
S19.16 | Clock systems | No
S19.17 | Emergency lighting systems | No
S19.18 | Specialist lighting | Sum
S19.19 | Earthing and bonding | Sum
S19.20 | Permits, testing, identification, ‘As Built’ drawings, manuals and builders work | Sum
S20.01 | Passenger lifts | No
S20.02 | Goods lifts | No
S20.03 | Dumb waiters | No
S20.04 | Passenger escalators, travellators, goods escalators and conveyors | No
S20.05 | Gantry cranes, including support structures, e.g. rails and corbels | No
S20.06 | Hoists | No
S20.07 | Building maintenance units | No
S20.08 | Permits, testing, identification, ‘As Built’ drawings, and maintenance manuals | No
S20.09 | Builders work | Sum

## Slide 49
Page 49
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
S21.01 S21.02 S21.03 S21.04 S21.05 S21.06 S21.07 S21.08 S21.09
Gases and compressed air services
Liquids of various types, supply and waste systems Fume extraction systems
Pneumatic and vacuum tube systems
Local refrigeration and cool room installations
Sanitary and refuse incinerator and disposal systems, including waste disposal units Specialist kitchen equipment, including hoods, ducts and fans
Specialist laboratory equipment Communication systems
(i)
(ii)
(iii)
(iv)
Internal call systems Telephone systems Radio and TV systems
Data networks
S21.10
Protective systems (excluding fire)
(i)
(ii)
(iii)
Security systems
Lightning conductor systems
Emergency staged evacuation systems
S21.11 S21.12 S21.13
NZIQS Elemental Analysis
List of Groups, Elements, Sub-elements: Element Unit Rate Record Sheet
S21.14
S22.01 S22.02 S22.03 S22.04 S22.05 S22.06 S22.07 S22.08 S22.09 S22.10 S22.11 S22.12 S22.13 S22.14 S22.15 S22.16 S23.01 S23.02 S23.03 S23.04 S23.05 S23.06 S23.07 S23.08 S23.09 S23.10 S23.11 S23.12 S23.13 S23.14 S24.01 S24.02 S24.03 S24.04
Building management systems Traffic control systems
Stoves, refrigerators, washing machines, dryers, botttle coolers, ice makers, glass
and dish washing machines, etc.
Permits, testing, identification, ‘As Built’ drawings, commissioning, manuals and builders work
Stormwater drains
Soil drains Land drains Chemical drains Culverts
Stormwater outfalls Channels and gratings Cesspits and grease traps Inspection chambers Manholes
Soakholes Holding tanks Pumps Septic tanks
Sewage treatment plants
Permits, testing, identification, ‘As Built’ drawings and builders work Roads
Kerbing and channelling
Paths, terraces and paved areas Site retaining walls
Steps
Screen walls and fencing Flower boxes and planters Grading, seeding and planting Irrigation systems
Seats, furniture and the like
Pavement cross-overs
Plumbing services associated with this element Electrical services associated with this element Security systems associated with this element Verandahs
Covered ways Sun screens Canopies
No No No No No No No No No No No No No No No No No No No No
Sum
m m
m
m No m No No No No No No No No Sum m2 m m2 m No m No m2 m2 No No
No
m m

## Slide 50
Page 50
Elemental Analysis of Building Projects 5th Edition January 2017, © NZIQS
No
No No
m
S24.05 S24.06 S24.07 S24.08 | Balconies Sculptures and Artwork Murals and Plaques Signs and lettering | No No No No
S24.09 | Flagpoles | No
S24.10 | Swimming pools | No
S24.11 | Curtains and blinds | m
S24.12 | Curtain tracks | m
S24.13 | Sundry minor alteration work | Sum
S24.14 | Small isolated structures such as pump houses, transformer enclosures and the like | No
S25.01 | Site establishment | Sum or %
S25.02 | Temporary services | Sum or %
S25.03 | Site management and personnel | Sum or %
S25.04 | Plant and equipment | Sum or %
S25.05 | Scaffolding | Sum or %
S25.06 | Cranage | Sum or %
S25.07 | Hoardings | Sum or %
S25.08 | Messing, ablutions and site accommodation | Sum or %
S25.09 | On-site overheads | Sum or %
S25.10 | Indirect costs | Sum or %
S28.01 | Professional fees and disbursements | Sum
S28.02 | Direct contracts | Sum
S28.03 | Loose furniture and equipment | Sum
S28.04 | Client supplied material | Sum
S28.05 | Territorial authority approval or consent fees | Sum
S28.06 | Resource consent fees | Sum
S28.07 | Development contributions | Sum
S28.08 | Temporary accommodation | Sum
S28.09 | Removal or relocation costs | Sum
S28.10 | Marketing and sales costs | Sum
S28.11 | Legal fees | Sum
S28.12 | Tenant fit-out contributions | Sum
S28.13 | Land acquisition costs | Sum
S28.14 | Principal’s bond | Sum
S28.15 | Operator licenses | Sum
S28.16 | Development management fees and administration costs | Sum
S28.17 | Finance and funding costs | Sum
NZIQS Elemental Analysis
List of Groups, Elements, Sub-elements: Element Unit Rate Record Sheet